## Slide 1
Sierra Foothills
Research and Extension Center
Compost application field day
November 14, 2018

## Slide 2
Atmosphere carbon
760 Pg
Vegetation carbon
610 Pg
Soil carbon
2000 Pg
(or more)
Photosynthesis
Plant/tissue death
Microbe respiration
Notes: CO BENEFITS

## Slide 3
Managing soils for increased carbon content has many co-benefits:
Fertility
Water holding capacity
Soil stability
Sustainability
Productivity

## Slide 4: Grasslands hold considerable potential for soil C sequestration The majority of grasslands are degraded
23 million hectares in California (40% of the land area)
30% of US land area
30% of global land surface area
Notes: CA rangelands roughly store about 1-2 Pg C in the top meter;

## Slide 5
Amendments of livestock manure increased soil carbon by 50 Mg C ha-1 in the top meter of soil
Not amended
Amended
0
100
200
300
Soil Carbon (Mg C ha-1)
From Silver et al. In prep
Analysis of 35 fields (1050 samples) from Marin and Sonoma Counties
Notes: 50 Mg C = 183 Mg CO2e; over 10,000 ha that is almost 2 million MT

## Slide 6
Chart: 
| Agricultural Soil Management | Stationary Combustion | Mobile Combustion | Manure Management | Nitric Acid Production | Wastewater Treatment | Composting
 | 26.37 | 22.9 | 18.4 | 17.3 | 10.7 | 4.9 | 1.8
Chart: 
| Enteric Fermentation | Natural Gas Systems | Landfills | Coal Mining | Manure Management | Petroleum Systems | Wastewater Treatment | Rice Cultivation | Composting
 | 164.5 | 157.4 | 114.6 | 64.6 | 61.4 | 25.2 | 15 | 8.3 | 2
Livestock manure is a large source of greenhouse gases
x10
U.S. Methane Emissions (MMT CO2e)
U.S. Nitrous Oxide Emissions (MMT CO2e)
U.S. EPA EPA 430-R-15-004 2013; Owen and Silver 2015 Global Change Biology
Notes: Note composting has lower emissions

## Slide 7
-1
0
1
2
Grazed and manured
Grazed
Methane
Nitrous oxide
Soil C
Net Balance
Climate impact (Mg CO2e ha-1 y-1)
From 2012 to 2100, manure applications led to a large net source (positive values) to the atmosphere
Owen et al. 2015, Global Change Biology
Source
Sink

## Slide 8
One time application
Did not increase field nitrous oxide and methane emissions
Created a slow release organic fertilizer
Composted organic matter
has much lower emissions

## Slide 9
Net primary production (a.k.a. forage production) increased every year following a one time compost application
Aboveground Net Primary Production (g m-2)
control
compost
Chart: 
 | 460.6467 | 512.5747 | 410.8371 | 220.6617
 | 736.9205 | 812.7955 | 844.8106 | 356.9197
Year
2009 2010 2011 2012
Ryals and Silver 2013 Ecological Applications, Silver et al. in prep.

## Slide 10
Chart: 
| 2008 | 2009 | 2010 | 2011 | 2012
Control | 2187 | 2867 | 1954 | 2312 | 2172.6068
Compost | 2334 | 3563 | 2615 | 2728 | 2514.373
Soil organic carbon (g m-2)
Compost amendments also significantly increased
soil carbon pools
Ryals et al. 2014 Soil Biology and Biochemistry; Silver et al. in prep

## Slide 11: Carbon sequestered in soil: 3 Mg C/ha over three years

## Slide 12
At a rate of 0.5 Mg C ha-1 y-1
= 21 MMT CO2e y-1
Units:
Mg = Metric ton
MMT= Million metric tons CO2e = CO2 equivalents
Emissions data: CA GHG Inventory 2013
Using half of California’s grasslands
Livestock (enteric fermentation)
~ 12 MMT CO2e y-1
Commercial/residential
~ 43 MMT CO2e y-1
Electrical generation (in state)
~50 MMT CO2e y-1
Notes: There is considerable potential to offset some of California’s energy use with soil C sequestration

## Slide 13
Ryals et al. 2016 Ecosphere
There were no significant changes in diversity

## Slide 14
SFREC
Solano
San Joaquin
Tulare
Mendocino County
Marin County
San Diego County
Santa Barbara County
Scaling up: testing the impacts of compost across California rangelands
What is the impact of predicted climate changes on rangeland carbon dynamics with and without compost amendments?

## Slide 15
Healthy Soils Project
Compare and contrast different types of compost for:
Forage production and species
Soil carbon sequestration
Soil moisture dynamics
Greenhouse gas emissions

## Slide 16
USDA Drought Project
Determine the effects of drought on:
Forage production and species
Soil carbon sequestration
Soil moisture dynamics
Greenhouse gas emissions
And interactions with nitrogen fertilization