## Slide 1: Ventura County Specific Field Fumigation Conditions Chloropicrin and Chloropicrin Containing Products

## Slide 2: Outline
Chloropicrin
  Quick Background and Facts
New Chloropicrin Conditions Announced by DPR
  Larger Buffer Zones
  Buffer Zones -Methyl Bromide and Chloropicrin
  Minimum Buffer Zones
  Limiting Acreage 40/60
  Notice of Intent Requirements
  Notification
  Fumigation Time Restrictions
  Buffer Zone Credits Allowed
  Ventura County Approved TIF Tarps for Buffer Zone Credits / Chloropicrin
    Interim TIF Tarp List Ventura County
    Micro Sprinklers “Sprinklers in Place”
Fumigating glasshouses with chloropicrin using an injection rig mounted on a Ransomes MG6 tractor 1960.

## Slide 3: Background
Chloropicrin, or trichloronitromethane, is a dense, pale yellow liquid that decomposes when heated to ≥112 ºC. Its property as a lachrymator prompted Germany to use it as a tear gas against the Allied forces during World War I—one of the first uses of a chemical weapon.
In 1848, Scottish chemist J. Stenhouse prepared chloropicrin by treating picric acid with sodium hypochlorite. Nitro groups were the only parts of the picric acid molecule to be used in chloropicrin, but the “picrin” name stuck. Today, chloropicrin is manufactured by the reaction between nitromethane and sodium hypochlorite.
Notes: 112 C is 233.6 F

## Slide 4: Chloropicrin Quick Facts:
In 2012 chloropicrin was used on about 67,000 acres in California
The Golden State has more than 9 million acres of irrigated land for farming according to the California Department of Conservation

## Slide 5: Chloropicrin Use Ventura County
2012 Chloropicrin
  1,889,235 LBS
  9,607 Acres
2013 Chloropicrin
  1,532,282 LBS
  7,926 Acres
2014 Chloropicrin
  1,764,243 LBS
  8,441 Acres
2012 Methyl Bromide (Combination)
  652,598 LBS
  2,373 Acres
2013 Methyl Bromide (Combination)
  393,486 LBS
  1,251 Acres
2014 Methyl Bromide (Combination)
  561,645 LBS
  2,036 Acres
Notes: 100% chloropicrin for total pounds used- not including other fumigants when used in combination

## Slide 6: New Chloropicrin Conditions Announced by DPR
Larger buffer zones
Buffer Zones (BZ) for chloropicrin have been developed by DPR which are often larger than current labels. Use DPR’s BZ look-up tables (appendix K) in combination with the label to determine the most restrictive buffer zone distances at:
http://www.cdpr.ca.gov/docs/enforce/compend/vol_3/append_k.pdf
Notes: DPR has developed buffer zones for chloropicrin that are often larger than the ones currently required by the United States Environmental Protection Agency (U.S.EPA) label. In some cases the new buffer zones have doubled in size. Larger buffer zones will apply when Totally Impermeable Film (TIF) tarps are not used. TIF tarps are a technological advance that is more effective in controlling fumigant emissions in soil. A buffer zone is an area that surrounds a field that has been treated with a pesticide; certain activities are restricted within the area for a specified period of time to protect human health.

## Slide 7: New Chloropicrin Conditions Announced by DPR
Buffer Zone Credits
Buffer zone reduction credits are allowed for approved tarp usage only. In contrast, label buffer zone reduction credits are not allowed for symmetry application systems, post-application water treatments, potassium thiosulfate, soil organic matter or clay content, or soil temperature.

## Slide 8: New Chloropicrin Conditions Announced by DPR
Buffer Zones for Methyl Bromide and Chloropicrin Combination
For products containing methyl bromide and chloropicrin, determine the methyl bromide and chloropicrin buffer zones separately. Determine the methyl bromide outer and inner buffer zones distances following the procedure described in “Methyl Bromide Soil Fumigation Buffer Zone Determination” at:
http://www.cdpr.ca.gov/docs/emon/methbrom/buffer_determination.pdf

## Slide 9: Determine the chloropicrin buffer zone using the appropriate label or DPR buffer zone table. These determinations will result in three possible scenarios for buffer zone restrictions:
If: | Then:
the chloropicrin buffer zone is smaller than both the methyl bromide inner and outer buffer zones… | only the methyl bromide inner and outer buffer zone distances and permit conditions apply
Scenario 1:

## Slide 10
Scenario 2:
If: | Then:
the chloropicrin buffer zone is larger than the methyl bromide inner buffer zone, but smaller than the methyl bromide outer buffer zone… | there are two buffer zones – a chloropicrin buffer zone and a methyl bromide outer buffer zone. The chloropicrin buffer zone distance also functions as the methyl bromide inner buffer zone distance. Both the chloropicrin buffer zone and methyl bromide inner buffer zone restrictions apply. All of the methyl bromide outer buffer zone restrictions also apply

## Slide 11
Scenario 3:
If: | Then:
the chloropicrin buffer zone is larger than the outer methyl bromide buffer zone… | there are two buffer zones – a chloropicrin buffer zone and a methyl bromide inner buffer zone. All of the methyl bromide inner buffer zone restrictions apply. The chloropicrin buffer zone distance also functions as the methyl bromide outer buffer zone distance. Both the chloropicrin buffer zone and methyl bromide outer buffer zone restrictions apply, except, no persons are allowed within the buffer zone except to perform fumigation-handling activities or transit by vehicle or bicycle

## Slide 12: Minimum buffer zone distance:
Tarps that qualify for a reduction credit of 60% | Tarps that do not qualify for a reduction credit of 60% |  | Untarped applications
 | Application block Less than or equal to 6 acres | Application block Greater than 6 acres, up to 40 acres | 
25 feet | 60 feet | 100 feet | 100 feet
Minimum buffer zone distances regardless of credits:
Notes: All untarped applications approved will maintain a min. buffer zone distance of 100 feet.

## Slide 13
DPR Notice of Intent Requirements:
  at least 48 hours before the scheduled application
Agricultural Commissioner’s Office
  at least 3 business days prior to the start of the fumigation
  applicator must obtain written approval of the NOI from the Agricultural Commissioner’s Office
  If the fumigation does not begin within 12 hours of the scheduled start time, a new NOI must be submitted and approved
New Chloropicrin Conditions
Announced by DPR
Notes: Notice of intent requirements: DPR will require upcoming fumigation at least 48 hours before the scheduled application. Current regulation requires a 24-hour notice.
Agricultural Commissioner’s Office- NOI must be received by the at least 3 business days prior to the start of the fumigation. Prior to fumigation, the applicator must obtain written approval of the NOI from the Agricultural Commissioner’s Office. If the fumigation does not begin within 12 hours of the scheduled start time, a new NOI must be submitted and approved.

## Slide 14: 3 Business Days-NOI’s
2014- May through October - 401 field fumigation NOI’s submitted
Re-submittals or amendments
2-3 inspectors managing the process/evaluating NOI’s

## Slide 15: Emergency Preparedness and Response Measures (EPRM)
If Response Information for Neighbors is chosen, it shall be recorded on the Notification Log (form VCAC-2015-2) and included with the NOI.
Acceptable Methods
  United States Postal Service
  hand deliver
  door hangers
  notifying homes which may be vacant
  All notifications shall be in English and Spanish

## Slide 16: New Chloropicrin Conditions Announced by DPR
Fumigation time restrictions – change from proposal
Labels have no restrictions on fumigation time
All other factors being equal, higher air concentrations occur at night due to inversions and more stable atmosphere
To help avoid peak flux at night for non-TIF and untarped fumigations
Applications must start no sooner than 1 hr after sunrise
Applications must end no later than 3 hrs before sunset
TIF fumigations have no time restrictions

## Slide 17: New Chloropicrin Conditions Announced by DPR
Maximum acreage
Non-TIF/untarped: 40 ac
County List -TIF: 60 ac – change from proposal

## Slide 18: New Chloropicrin Conditions Announced by DPR
Buffer zone distances: reduction credits
Labels reduce buffer distances up to 80% using 11 possible “credits” for conditions and practices with lower emissions
DPR recommends 1 credit: 60% credit for TIF tarps
Tarps assigned 60% credit require EPA and DPR approval

## Slide 19: Volatile Organic Compound Emission's (V.O.C.’s)
2012 May through October
  V.O.C.’s emission’s total for Ventura County 826,904 LBS
  87.8 % of total allowance
  Allowance = 942,000 LBS
2014 May through October
  V.O.C.’s emission’s 324,913 LBS
  34.3% of total allowance
  Allowance= 948,000 LBS

## Slide 20
County approved TIF Tarps for Chloropicrin
60% Buffer zone reduction
AEP-one, clear, EVOH barrier, 1.0 mil | Raven TIF VaporSafe™ ≥ 1 mil
Berry EVOH-High Barrier, black, 1.25 mil | TRM Manufacturing Weather-all Power Film HB 125, custom, ≥ 1.25 mil
Berry EVOH-Supreme Barrier, black, 1.25 mil* (Not approved for use with MBr) | TRM Manufacturing Weather-all Power Film HB 125, clear, ≥ 1.25 mil
Berry Plastics TOTAL BLOCKADE TIF, white/black, 1.25 mil | TRM Manufacturing Weather-all Power Film HB 125, black, ≥ 1.25 mil
Berry Plastics TOTAL BLOCKADE TIF, white, 1.25 mil | TRM Manufacturing Weather-all Power Film HB 125, white, ≥ 1.25 mil
Berry Plastics TOTAL BLOCKADE TIF, green, 1.25 mil | TRM Manufacturing Weather-all Power Film HB 125, green, ≥ 1.25 mil
Berry Plastics TOTAL BLOCKADE TIF, brown, 1.25 mil | TRM Manufacturing Weather-all Power Film HB 125, brown, ≥ 1.25 mil
Berry Plastics TOTAL BLOCKADE TIF, black, 1.25 mil | TRM Manufacturing Weather-all Power Film HB 125, black/white, ≥ 1.25 mil
Berry Plastics TOTAL BLOCKADE TIF, silver/black, 1.25 mil | TRM Manufacturing Weather-all Power Film HB 125, black/silver, ≥ 1.25 mil
Guardian TIF ≥ 1.1 mil, embossed | TRM Manufacturing Weather-all Power Film HB 125, black/clear/black, ≥ 1.25 mil
Notes: County approved TIF Tarps for Chloropicrin - 60% Buffer zone reduction
DPR has informed us that some of the 60% credit tarps on the US EPA approved list may not perform as expected in high humidity. Currently DPR is establishing an approved list that will be a subset of the US EPA approved list. It may take some time for DPR to establish the California approved list. In the interim, refer to the list (below) of tarps that have been tested and qualify for 60% reduction in buffer zone distance.
PLEASE KEEP IN MIND: When DPR’s TIF approved tarp list for 60 % buffer zone reductions are determined, this may change current approved TIF tarps on the **county approved list for 60 % buffer zone reduction. See county list below.
**At this time the following tarps are approved for use with field soil fumigants containing chloropicrin in Ventura County and qualify for 60% credit. The mils listed for tarp thickness are the minimum allowed:

## Slide 21: Sprinklers in Place
Meeting held on March 4th 2015 discussing micro sprinklers
  Discussed odor suppression through the use of micro sprinklers
  Grower’s are using micro sprinklers more with drought situation
  Agricultural Commissioner- Henry Gonzales- confident in our TIF list and combination micro sprinklers for odor suppression
  The requirement of “Sprinklers in Place” – same as past years
  Outcome:
  ***Micro Sprinklers (if used with county approved TIF tarp list) MEET requirements of “sprinklers in place” for odor suppression***

## Slide 22: Thank You!
Ryan Casey
Deputy Commissioner
Ventura County Agricultural Commissioner’s Office
805-388-4222 X 7132
ryan.casey@ventura.org