## Slide 1: Prescribed Burning: Smoke Management Regulations
Doug Carson
Air Pollution Control Specialist II
Calaveras County Air Pollution Control District

## Slide 2: Air Pollution Regulatory Framework
Federal – U.S. Environmental Protection Agency
  Clean Air Act (1970 with amendments in 1990)
State – California Air Resources Board
  California Clean Air Act – 1988
Local – Air Pollution Control & Air Quality Management Districts
  Local Rules and Regulations
  Stationary sources of air pollution
Notes: Federal Clean Air Act
  National Ambient Air Quality Standards
  Planning requirements for attaining air quality standards
  Interstate commerce
California Clean Air Act and Health & Safety Code
  More restrictive ambient standards
  Planning
  Rulemaking
  Enforcement
  Public Outreach
  Agricultural Sources
  Portable Equipment
  Air Toxic Sources
  Incentive Programs such as Carl Moyer
  Mobile Sources and Fuels (some District crossover)
  Stationary Sources (some District crossover)
  Next slide is a transition into air quality standards.

## Slide 3: Major Ozone Precursors Sources
Notes: We have both Man-made and Natural Sources of air pollution
Some Natural include Geo-genic, as in from soil/rocks
Bio-genic is from plants. As an aside liquid amber trees and many oaks have high biogenic emissions
We have both federal and state standards for air pollutants
Ozone or more commonly called smog is created by two chemicals, mixed with high temperatures.

## Slide 4: major pm sources
Notes: We have state and federal standards for particulate matter.

## Slide 5: particle size
Notes: PM 10 and PM 2.5

## Slide 6
How pollutants affect our health
Notes: Health Affects such as:
Airway Inflamation
Effects on Lung Function
Increased Susecptability to Respitroy Infection
Vascular Inflamation
Take home is very small PM2.5 particles can get into one’s lungs and then more than likely don’t come out.

## Slide 7: California Air districts
Calaveras County
35 Air Districts
Notes: 35 - Air Pollution Control Districts (APCDs) and Air Quality Management Districts (AQMDs)
Board of Directors/Board of Supervisors
Operating revenues can come from any combination of the following:
Fees
Designated funds from the US EPA (fyi, that’s subvention)
state DMV
local mitigation funds and
per capita assessment

## Slide 8: Air District Programs
Permitting and Inspections
CEQA and Land Use Mitigation
Air Quality Planning
Incentive Programs
Public Information
Smoke Management Program
Notes:   Stationary sources, portable equipment, and complaints
  Environmental review and commenting for land use projects; dust control plans
  Air Quality Management Plans, State Implementation Plans, Rule Development, air monitoring, and emission inventories
  General education and outreach, media relations, advisories and press releases
  Agriculture burning, backyard burning & prescribed fire

## Slide 9
Notes: Typical burn pile
Illegal burn
Ag Burning (rice stubble in Sacramento Valley)
Prescribed burn on Cal Fire’s property – Mt. Howell, Colfax

## Slide 10: Agricultural Burning Regulations
California Health & Safety Code Article 3 – Section 41850 Agricultural Burning administered through the Title 17 California Code of Regulations-Subchapter 2 Smoke Management Guidelines for Agricultural and Prescribed Burning
Prescribed burning is the planned application and confinement of fire to wildland fuels on lands selected in advance of that application to achieve specific identified objectives.
Prevention of high intensity wildland fires
Watershed Management
Range Improvement
Vegetation Management
Forest Improvement
Wildlife Habitat Improvement
Air Quality Maintenance
Planned Application of Fire
Submittal of a Smoke Management Plan
District Rules – Smoke Management of Prescribed Burning
Burn Permit Issued and Fees Paid
Smoke Management Program
Notes: California Health and Safety Code:
Defines Agricultural Burning which includes Prescribed Burning
Same definition in the Public Resources Code (CAL FIRE’s), changed in 2004
Requires District to adopt a Smoke Management Program which is approved by the state
District Rules also may have the same language that the state requires, but may not depending if they are updated or not.
Regardless, the state rules on this are required to be followed as per the adopted program
Submittal of a Smoke Management Plan which will be covered more in-depth shortly
Issuance of a burn permit. Each District may be a bit different.
And in some cases there could be burn permit fees associated

## Slide 11: Title 17 CCR Smoke Management Guidelines
Required each air district to adopt a Smoke Management Program
Planning: submits a Smoke Management Plan (SMP)
Permitting: Air District may issue a Burn Permit or a different type of approval for the SMP
Authorization: Based on the burn day status, the Air District authorizes burning
Use Prescribed Fire Information Reporting System (PFIRS) to manage our burn program
Notes: Title 17 is ultimately a communication program
Planning
Permitting
Authorization System
Can use an online system PFIRS

## Slide 12: Program Objectives
Minimize smoke impacts to the public and the air shed
  Allows for the continuation of agricultural and prescribed burning as a resource management tool
  Provides increased opportunities for agricultural and prescribed burning
  Helps in the prevention of catastrophic wildfires by reducing vegetation through burning

## Slide 13: When is a Smoke Management Plan Needed?
Four levels to determine if and how much of a SMP is or is not needed.
Less than 1 ton of Particulate Matter and/or less than 10 acres (see end of handout)
1 to 10 tons of Particulate Matter and/or 10 to 100 acres
10 tons of Particulate Matter and/or over 250 acres
Regardless of size and Particulate matter, potential to impact a smoke sensitive area
Contact your air district to help decide the level needed
Notes: PM 10 was the regulatory level at the time that the regulations were created and have not been changed. Calculations are part of the SMP handed out.

## Slide 14: What is Needed for a Smoke Management Plan (SMP)? (How Much Smoke is Expected?)
SMP Begins with Basic Information (Sec.1)
Landowner Information
  Name
  Address
Prescribed Burn Staff Contact Information
Alternative Contact Information
Map of the location
Notes: Planning

## Slide 15: Project Information and Location Information (Sec. 1)
Type of Burn
  Broadcast/Understory - Acres
  Piles – Machine/Hand piles and how many
    Any Stumps?
    Dirt in the piles?
Vegetation Type – What is being Burned?
How Dry/Wet is the Vegetation? (Fuel Moisture)
How long is the burning expected to last?
Is the burn on a slope and what is its aspect - topography?
How much PM10 will be created?
Notes: Type of Burn:
Underburn/Broadcast
Machine Piles how are they built – with a brush rack to keep out dirt
Stumps can be burned but with the caveat: Free from dirt, split at cut point if over 12” diamater
Stumps need a lot of fuel to burn.
Hand piles
Vegetation to be burned. How big?
When was it cut? Dry vegetation burns better than wet (woodstove firewood example)
How long will it burn?
Slope can determine how a burn travels, up or down hill
Aspect – South drier North wetter

## Slide 16: Smoke Sensitive Areas Public Notification (Sec.1&3)
Where are the closest neighbors?
  Direction and Distance
Are there any places close that could be impacted by smoke?
Public Notification Contact Methods
  Telephone
  Email
  Flyers
  Social Media – Next Door or Neighborhood Facebook Page
  Signage
Notes: Next is Smoke Sensitive Information and Public Notification

## Slide 17: Weather – Ignition Prescription Where will the Smoke Go? (Sec. 1&2)
Burn Days
  Marginal?
Wind Speed and Direction
  Forecasts
  Surface and Transport Winds
Specific Temperature
Time of Day for Burning
  Morning – Evening Variations
  Inversions
Relative Humidity
Notes: Weather – Ignition Prescription: Where will the Smoke Go?
Burn Days:
No Burn
Burn Day:
Marginal
Fair
Good
Superior
FYI: No Burn Day is based on whether smoke will linger
CARB meteorologists call it based on:
  Surface winds
  Transport winds
  Inversions/Heights
  Forecast
  Population densities
APCD may also call it based on local factors
CalFire may also call it based on fire conditions
Wind Speed and Direction – where will the smoke go
Need a specific temperature for burning?
Time of day and Relative Humidity.

## Slide 18: Smoke Mitigation (Sec.2)
What happens if Smoke Becomes a Problem?
What Contingencies are Considered?
    Is there a containment line?
    Stop lighting
    Allow burn down
    Have Water
    Consider Mopping Up
    Get it all lit faster
How will you Monitor Smoke? (Sec.4)
Work with Air District Staff
Notes: Go / No Go is up to Land Owner/Manager

## Slide 19: SMP Complete – What’s Next
SMP Submitted to District
District Approves – Disapproves
District issues Air District Burn Permit
Wait for Burn Day to Burn
Request Approval for Ignition Day of Burn (Sec.5)
Notes: Go / No Go is up to Land Owner/Manager

## Slide 20: Monitoring Smoke Conditions
What is the Plume doing?
Where is it going?
How high is it getting?
Could the neighbors be getting too much smoke?
Post-burn report (Sec.6)
Notes: Go / No Go is up to Land Owner/Manager

## Slide 21: Technical Tools
PFIRS – Prescribed Burn Information Reporting System
Control Burn Notices (aka burn day)
Sacramento Valley Acreage Allocation
Fire Information Map
  Integration of Air Monitoring Information - Statewide
  Wildfire Information - Wildfire smoke affects allocation

## Slide 22: What is PFIRS ?
Prescribed Fire Information Reporting System
  Communication tool
  Interactive mapping
  Not a regulatory tool
Notes:   What is PFIRS?
  Interfaces between air quality managers, land management agencies, and individuals that conduct prescribed burning in California
Provides a map of current projects
    What burns are planned?
    What burns were occurring?
Contains a database on smoke management plans, burn approvals, & emissions information
Shows information statewide: if the public sees smoke, by looking at the map you can see if it’s from a prescribed burn
We use it because its less paper, but for some a paper version of the SMP works better. We would work with folk on what would be the best choice to use.

## Slide 23: PFIRS Overview
Land Manager Use
Request An Account
Fill in SMP application
Review SMP
Approve SMP
Approve Ignitions

## Slide 24
Notes: Started as a tool where prescribed burns could be viewed on a map both valley-wide and state-wide
Land Managers input project information

## Slide 25: Request an Account

## Slide 26: PFIRS: ARB Products

## Slide 27
Notes: Burn Day Criteria established by the Air Resources Board
Factors affecting No Burn Days:
  Weather – inversion layers
    Warm air aloft sinks; as it continues warm it becomes more stable, creating an inversion over the cooler air below it.
    Inversion (the stable air) acts like a lid on the pollution below not allowing it to mix and disperse
    Stability is a measure of the atmosphere’s ability to lift smoke away from the ground
    More stable less smoke rise - Less stable better smoke rise
  Poor air quality or “Spare the Air Day”
  Fire safety
    High fire hazard declared by local fire agencies/CAL FIRE

## Slide 28: PFIRS: Fire Information Map
Provides real-time
information

## Slide 29: Collaboration is KEY
Continue to protect Air Quality while providing for opportunities to dispose of vegetation by burning where appropriate.
Continue to strive towards achieving and maintaining air quality standards
Work with those conducting prescribed fire operations to minimize, smoke impacts on the public.
Maintain good working relationships with cooperators.

## Slide 30: Helpful Websites
Prescribed Fire Information Reporting System: https://ssl.arb.ca.gov/pfirs/index.php
California Local Air District Directory http://www.capcoa.org/districts/
Northern and Southern Predictive Services https://californiasmokeinfo.blogspot.com/p/fire-potential_27.html
National Weather Service https://www.weather.gov/