## Slide 1: Juice Nutrient Analysis and Additions: Methods and Consequences
Linda F. Bisson
Department of Viticulture and Enology
Quality Control Management during Crush and Fermentation
August 7, 2014

## Slide 2: Critical Nutrients for Fermentation
Nitrogen
Phosphate
Vitamins
Potassium

## Slide 3: Yeast and Nitrogen

## Slide 4: Nitrogen Is Required For:
Protein and nucleic acid synthesis: the creation of new cells
Maintenance of metabolism: replacing enzymes and catalysts past their prime
Adaptation to new environments: getting rid of no longer useful enzymes and replacing them with ones more fit for the environment
Stress tolerance: formation of cofactors and enzymes allowing survival in presence of stressors

## Slide 5: Nitrogen Is Needed at All Stages of Yeast Growth
Lag Phase: to adapt from lag phase to active growth
Growth Phase: for building blocks and catalysts
Stationary Phase: for production of survival factors
Dormant Phase: to survive periods of severe growth inhibition

## Slide 6: Timing of Nitrogen Addition
Depends upon starting level of nitrogen:
  Need N to adapt to juice or to build up starting populations
  Sufficient N to build initial population
  Sufficient N to sustain fermentation
Depends upon presence of competition:
  What other organisms are present?
  How competitive are those organisms (population sizes? pH?)
Depends upon starting sugar level/final ethanol:
  Higher potential ethanol requires higher N levels
Depends upon yeast strain and innate set-points:
  Native versus commercial inoculum
  Presence of other stressors

## Slide 7: What Type of Nitrogen Source Is Best?
A mixture!
  Minimizes need to make biosynthetic enzymes
  Conserves energy
  Enables cofactors to be deployed elsewhere
Sole nitrogen sources
  Value depends upon how quickly the nitrogen contained in the molecule can be mobilized
  Depends upon how easily that compound can be interconverted into other compounds

## Slide 8: Yeast Nitrogen Biology
Yeast have nitrogen sensing mechanisms and will adapt growth fermentation activity to match available nitrogen
The lower the nitrogen the slower both growth and fermentation will be
At too low of a concentration yeast will shut down metabolism
At too high of a concentration yeast will also shut down metabolism
Response to nitrogen is dependent upon presence and availability of other nutrients
Everything is intricately related via a complex regulatory network

## Slide 9: Yeast Nitrogen Biology
A complex regulatory network means yeast strains will vary in their response to nitrogen availability
High and low N-demanders generally have different regulatory set points for N excess and limitation

## Slide 10: Yeast Nitrogen Sources
Ammonia
Most amino acids
Degradation may depend upon availability of other components: vitamins and oxygen
Utilization impacted by other environmental factors such as pH and ethanol

## Slide 11: Special Case: Native Fermentations
Nutritional requirements of cells present not known
More typically than not, a mixed population of Saccharomyces and non- Saccharomyces
Saccharomyces population is not going to be uniform

## Slide 12: Special Case: Mixed Populations
More competition for nutrients
Accumulation of inhibitory end products
Non-homogeneity of Saccharomyces
  In some regions this leads to domination by less fermentatively robust strains = strong initiators are not necessarily strong finishers

## Slide 13: Mixed Populations
The Good News:
  Greater complexity
  Selection for survivalists
  Slower fermentations
The Bad News:
  Higher risk of something going wrong
  Need to pay closer attention than with commercial inoculants to nitrogen levels

## Slide 14: Viticultural Factors Impacting Nutrition
First source of nutrients
Can be a source of inhibition
Rot changes fermentation dynamics
Sometimes need to get yeast nutrition right in the vineyard, winery additions do not seem to compensate

## Slide 15: Nitrogen Measurement

## Slide 16: Monitoring Nitrogen Levels
Amino acid analysis (HPLC)
Free amino nitrogen (FAN)
NOPA (nitrogen by OPA)
Yeast Assimilable Nitrogen (YAN)
Yeast Non-Assimilable Nitrogen (YNAN)
Yeast Utilizable Nitrogen (Hefeverwertbarer Stickstoff)
FOSS
Mid Infrared spectroscopy (MIR)

## Slide 17: Monitoring Nitrogen Levels
Some methods are direct: NH3 and amino acids
Some methods are indirect and underestimate amino acid nitrogen but include non-assimilable N
Other methods suffer from interference
Historical knowledge of vineyard can inform N additions
Knowledge of yeast and N requirements important in informing N additions

## Slide 18: Juice/wine analysis
Yeast assimilable nitrogen (YAN)
    Ammonia (NH3) and free alpha amino nitrogen (FAN)
  How to measure?
    Formol titration (FAN + NH4+)
      Only need pH meter
    NOPA method (primary amino acids)
      Need spectrophotometer
      Derivatization of primary amino acid groups with o-phthaldehyde/N-acetyl-L-cysteine reagent
      Resulting iso-indole derivative absorb at 335 nm
      Quantification by using calibration curve using known iso-leucine concentrations
    FOSS (FAN + NH3)
    Send it out to a commercial analytical laboratory

## Slide 19: Yeast Assimilable Nitrogen (YAN) Levels in Juice
Vary by varietal, region and season
YAN: Free amino nitrogen (FAN) + ammonia
Range from low 60’s to over 500
Can vary two-fold across fermentation lots from the same vineyard and not in concert with Brix levels
FAN/YAN levels of each fermentation vessel need to be measured!

## Slide 20: Advice

## Slide 21: When to Measure?
During rehydration: available to yeast, stimulates adaptation
Initial juice: following YAN assessment
Early in fermentation: 24-48 hours post-inoculation
If fermentation rate is slower than expected
For Native fermentations, measuring periodically during fermentation is important

## Slide 22: Nitrogen Levels
INADEQUATE: < 80 PPM
DEFICIENT: < 125 PPM
SUFFICIENT: 145-275 PPM
EXCESSIVE: >500

## Slide 23: NITROGEN REQUIREMENTS: mg OF YAN NEEDED TO CONSUME 1g/L SUGAR
High variability in wine yeasts: above N requirements based on a 250g/L sugar
~150ppm ~200ppm ~225ppm ~300ppm
Notes: Group 2 need 150 ppm, Group 3 need 200ppm, Group 4 need 225ppm, group 5 need 300ppm Nitrogen to consume 250g/L sugar.

## Slide 24: What Is the Best Time for a Nitrogen Addition?
Is the population that will complete the fermentation dominant? Want to feed that population
  Is that the population present at time 0?
    Inoculated from a fermenting tank
  Is that the population present at time 48 hours?
    Inoculated from active dry yeast packet
  Are strain populations changing dynamically as ethanol increases?
    Uninoculated/native fermentation

## Slide 25: What Is the Best Time for a Nitrogen Addition?
How high is the ethanol level?
  High ethanol decreases amino acid transport
  Low pH, high ethanol and proton stress decreases ammonia uptake
Are there other deficiencies?
  Vitamin/mineral cofactor deficiency can impact amino acid metabolism (by preventing some reactions from occurring)
  Stress can drive up amino acid demands in cell (for glutathione production for example)

## Slide 26: Nitrogen Vitamin Interactions