## Slide 1: Taint Mitigation: Tricks of the Trade and Tasting #6
Chik Brenneman
UC Davis Department of Viticulture and Enology

## Slide 2: Background
Chemistries of sulfur formation are complex
#%&* Happens

## Slide 3: Winemaker Responsibilities
Avoid formation in the first place
  Careful attention to fermentation conditions
    Temperature
    Nutrients
    Additives
Address each situation promptly and effectively
  Identifying the taint
  Getting the wine to a stage at which you can treat it
  Understanding that the treatments have limitations/risks

## Slide 4: Winemaker’s Tool belt
Fermentative Issue – Sulfides
  Food if greater than 10 brix
  Aeration
Post Fermentation
  Sulfides
    Copper sulfate once the wine has been settled
  Mercaptans
    Copper sulfate
  Disulfides (DMDS, DEDS)
    Ascorbate > 50 mg/L then copper sulfate
  Blending

## Slide 5: TTB Rules on Ascorbate
Ascorbic acid iso-ascorbic acid (erythorbic acid): To prevent oxidation of color and flavor components of juice and wine
May be added to grapes, other fruit (including berries), and other primary wine making materials, or to the juice of such materials, or to the wine, within limitations which do not alter the class or type of the wine. 21 CFR 182.3013 and 182.3041 (GRAS).

## Slide 6: Winemaker Rules on Ascorbate use
Ascorbic Acid is an oxidant
Stabilize Free SO2 before proceeding
  Free = 31 mg/L
  Total = 114 mg/L
Understand that the reactions can be fairly slow at cellar temperatures

## Slide 7: TTB Rules on Copper Additions
Copper sulfate: To remove hydrogen sulfide and/or mercaptans from wine
The quantity of copper sulfate added (calculated as copper) must not exceed 6 parts copper per million parts of wine (6.0 mg/L). The residual level of copper in the finished wine must not exceed 0.5 parts per million (0.5 mg/L). 21 CFR 184.1261 (GRAS).

## Slide 8: Winemaker Rules on Copper Use
Use the lowest effective amount
Risk of haze formation
Act as an oxidation catalyst
React with volatile thiols thus muting desirable characters
Prophylactic additions are not recommended

## Slide 9: Today’s Wine
2014 Albariño/Alvarinho
  Juice Chemistry
    Harvested August 26, 2014
    24.7 Brix
    TA=3.39 g/L
    pH=3.75
    Ammonia = 43 mg/L
    NOPA=160 mg/L
    Malic Acid at harvest = 1.173 g/L
    Malic acid in the wine = 0.9 g/L

## Slide 10: Tasting Discussion
This was a student project
Problem was universal across most of the student projects that used this juice
Didn’t see this with other projects in which this juice was used.
  DAP juice addition of 4#/K was the main difference
Wines ‘morphed’ in the three weeks following our assessment on how this module was designed
Module was re-designed – Consider this Glass 1 thru 6
  Glass 1 is the control wine

## Slide 11: Is there a difference in the wines?
Glass 1 – Control Wine (Base 1)
Glass 2 – Base 1 + Ascorbate (100 mg/L)
Glass 3 – Base 1 + Copper (1 mg/L)
Glass 4 – Base 1 + Copper (6 mg/L)
Glass 5 – Base 1 + Ascorbate (100 mg/L) + Copper (6 mg/L)
Glass 6 – [Base 1 + Ascorbate (100 mg/L) + Copper (6 mg/L)] + Base 2

## Slide 12: Why were these additions chosen?
Demonstrate the chemistry and sensory chages associated with the treatment
Underscore the importance of the bench trial

## Slide 13: Closing Remarks
Even the best winemakers will encounter this problem
The best quality wines will be those that you have taken the time to
  Assess the problem
  Perform the appropriate bench trials
  Perform the appropriate post treatment analysis to ensure compliance and quality control
  Enjoy the wine