## Slide 1: Impact of Oxygen and Hydrogen Peroxide Treatments on Torrontes Aroma Profiles
Linda F. Bisson
Department of Viticulture and Enology
University of California, Davis
Wine Flavor 101 June 5, 2015

## Slide 2: Oxygen in Wine
Important for color and tannin maturation
Important for reduction/modification of astringency
Results in oxidized aromas
Enables growth of organisms
Results in loss of varietal character

## Slide 3: Goal of Study
Compare molecular oxygen/aeration treatments to spiked additions of hydrogen peroxide in juice prior to fermentation
Compare post-fermentation aeration and H2O2 treatments of treated and control juices.

## Slide 4: Key Questions
Do H2O2 and oxygen treatments have the same effects in juice and in wine?
Are wines made from juices exposed to oxygen/H2O2 more or less sensitive to subsequent oxygen/H2O2 treatments?
What are the progression of impacts on white wine aroma of oxidation treatments?

## Slide 5: Impact of Oxygen
In Juice
  Enzymatic oxidation enabled
  Chemical oxidation enabled
  Nutrient for microbes
In Wine
  Chemical oxidation enabled
  Potential for spoilage organism use

## Slide 6: Impact of H2O2
In Juice
  Chemical peroxide oxidation enabled
  Inactivation of SO2
  Potential for inhibition of microbial growth
In Wine
  Chemical peroxide oxidation enabled
  Inactivation of SO2
  Potential for inhibition of microbial growth

## Slide 7: Study Design
GRAPES
Control
Air
H2O2
Control
Control
Control
Air
Air
Air
H2O2
H2O2
H2O2

## Slide 8: Study Design
Torrontes grapes
Hydrogen peroxide treatment: 150 mL of 3% H2O2
Aeration treatment: 30 minutes of air circulation using the pump on the IFCS with the intake valve set to 5.5
No SO2 additions
Inoculation with the commercial yeast strain EC1118

## Slide 9: Juice Composition and Fermentation Conditions
Juice Analysis | 
Brix | 23.9
pH | 3.71
Titratable Acidity (g/L) | 3.97
NOPA (mg/L) | 136
Ammonia (mg/l) | 13
Yeast Assimilable Nitrogen (mg/L | 149
Fermentation Volume | 24.2 gallons
Fermentation Temperature | 17°C

## Slide 10: Oxidation Characters in Wine
Chemical Oxidation
  Cascade initiated by molecular oxygen
Enzymatic (biological) Oxidation
  Tryosinase (polyphenol oxidase) (plant)
  Laccase (Botrytis & molds)

## Slide 11: Oxygen and Chemical Oxidation
Molecular oxygen is a good oxidizing agent
(possessing an affinity for electrons)
O2 e O2- e O22- e OH e OH-
OH- + H+ H2O

## Slide 12: Oxidation Chemistry of Wine
Oxidation reactions may be “buffered” much like pH by components that readily donate or accept electrons
Glutathione, a tripeptide, is an important buffering agent in cells as it exists in an equilibrium between oxidized and reduced states
Oxidation reactions often are chain reactions and the oxidizing species may not be consumed but transformed into an even more reactive component or even regenerated

## Slide 13: Oxidation Chemistry of Wine
Catalysts present in wine impact extent and type of oxidation reactions occurring
Hydrogen peroxide is an intermediate produced during oxygen-induced oxidation but other reactive oxidative species are more common

## Slide 14: Oxidation Chemistry of Wine
Phenolic compounds can be oxidized in the presence of oxygen
Oxygen has limited reactivity towards phenolic compounds in its normal O2 form
Oxygen is “activated” by metal ion catalysts in the wine such as iron (Fe)
Oxidation in wine is caused by the formation of reactive oxygen species (ROS)
The hydroxyl radical ( OH) is the reactive agent

## Slide 15
Chemical Oxidation and the Formation of Acetaldehyde
Danilewicz 2007
Waterhouse and Laurie 2006
Waterhouse and Laurie 2006
Notes: 15

## Slide 16: Enzymatic Oxidation
OH O
R OH R O
PPO, O2

## Slide 17: Control of Enzymatic Oxidation
Use of sulfite to inhibit PPO (grape)
Use of yeast to consume oxygen until ethanol inactivates PPO
Laccase: Control mold in vineyard
Laccase: use of HTST (high temperature short time) treatment to inactivate enzyme
Bentonite fining of juice to remove enzymes

## Slide 18
Chemical Bridging by Oxidized Compounds
1 2 3 4 5
Notes: 18

## Slide 19: Oxidative Damage to Wine
Formation of off-colors (browning or pinking)
  From oxidation of tartrate to glyoxylic acid
  Formation of reactive quinones
Formation of oxidized flavors
Loss of varietal aroma

## Slide 20: Common Oxidation Reactions of Wine
Alcohols to Aldehydes
Organic Acids to Keto Acids
Reaction with thiols and loss of varietal character

## Slide 21: Acetaldehyde
Low concentrations: apple, green apple
Higher concentrations: nutty, pungent, chemical
Appearance indicates ethanol is being oxidized and wine should be protected from further oxygen exposure

## Slide 22: Fusel Aldehydes
Fusel alcohols (oils) are made during amino acid degradation
Fusel alcohols can be reoxidized to aldehydes during aging
Recent experiments suggest fusel aldehydes may be important “impact” compounds in wine

## Slide 23: Fusel Aldehydes
Isobutyraldehyde: banana, acrid, pungent
Isovaleraldehyde: nutty, fruity, cocoa, acrid, pungent
2-Methyl butyraldehyde: aldehydic, berry, choking, cocoa, musty

## Slide 24: Findings from Study
All treatments derived from juice aeration arrested at a high RS level:
  Air:Control: 13.75 g/L sugar
  Air:Air: 12.72 g/L sugar
  Air:H2O2: 16.21 g/L sugar
H2O2 treatment did not impact fermentation rate or progression
Significant aroma differences were detected
  Some loss of varietal aroma
  Some dominance of yeast characters

## Slide 25: Acknowledgments
VEN124 Students
  Michael Attanasi
  Sean Eridon
  Chris Johnson
Chik Brenneman

## Slide 26: Tasting
GRAPES
Control
Air
H2O2
Control
Control
Control
Air
Air
Air
H2O2
H2O2
H2O2

## Slide 27: Torrontes Tasting
Glass 1: Control juice; no wine treatment
Glass 2: Control juice; air wine treatment
Glass 3: Control juice; H2O2 wine treatment
Glass 4: Air Juice; no wine treatment
Glass 5: Air juice; H2O2 wine treatment
Glass 6: H2O2 juice; no wine treatment