## Slide 1: A Convenient Truth Composting for the home gardener
Don Krafft
Sara Johnson
UCCE Composting Education Program

## Slide 2
Anatomy of America’s garbage
https://www.epa.gov/
The concept of waste was invented by humans

## Slide 3: Waste management hierarchy
Reduction | Buy and acquire sustainably. Don’t buy too much. Avoid unneeded materials
Re-use | Re-use items and materials in their current state. Re-purpose. Give away. Sell
Recycling | Re-create similar materials using municipal recycling services
Composting | Return nutrients to the soil by micro-biotic decomposition
Recover | Recover energy from waste by capturing methane and other industrial gases
Residuals | Deposit unwanted materials in a landfill
Most preferred
Least preferred

## Slide 4: The Fate of Organics
Landfill | Anaerobic Digestion | Composting
Single stream mixed with trash Requires alternative Daily Cover of soil | Small ‘Village’ scale Large Private or Public e.g. Zanker Recycling | Backyard or Home scale Community Scale Large-scale Municipal or Private e.g. Z-Best Products, Gilroy

## Slide 5: Why compost?
Improves soil fertility
  Increases nutrient-holding capacity
  Reduces need for chemical fertilizer
Waste diversion
  Reduces methane emissions
  Increases water retention and quality
  Reduces irrigation requirements
Carbon sequestration
  Creates stable forms of carbon
Pathogen suppression
  Provides bio-filtration
  Supports beneficial microbes

## Slide 6: https://www.planetnatural.com/tumbling-composter/
Soil consists of
  Decomposed organic matter
  Sand, silt, clay
Soil fertility comes from
  Minerals
  Microorganisms
  Organic matter
  Olmec, Fluvic, and Humic acids
Soil fertility
Compost is nature’s way of recycling
From
compost
Notes: -Is compost a fertilizer: It is a soil amendment with time-released nutrient benefits
-N-P-K is approximately 1-1-1
-Compost depends on microbial life present within the material to be effective
-Guess number of microbes in a teaspoon of soil – about same number of people on earth. 7 1/2 Billion (Bacteria, Actinomycetes, Fungi, Algae, Protozoa, Nematodes)

## Slide 7: Is compost a fertilizer?
The big three plant nutrients N ▢ P ▢ K
  Nitrogen ▢ Phosphorous ▢ Potassium % by weight
N ▢ P ▢ K values for compost
  0.5 % to 1.0 %
Fertilizer must have a guaranteed analysis
Compost is an amendment
Plants and microbes have been “doin’ it” for a long time

## Slide 8: How to make compost
Browns
Greens
Air
Moisture
Finished compost
https://www.grow-it-organically.com/build-a-compost-pile.html
http://clipartix.com/calendar-clipart-image-3592/
https://www.pinterest.com/pin/490470215645748858/
Microbes + Time

## Slide 9: Composting materials
50% Input “green” feedstock (nitrogen)
  Manure
  Grass clippings
  Food scraps
  Green plant cuttings
  Coffee grounds
  Eggshells
50% Input “brown” feedstock (carbon)
  Cardboard
  Newspaper
  Straw
  Dry leaves
  Sawdust (not treated)
  Woody cuttings
50%
50%
Other proportions can be used for specialized applications

## Slide 10: Materials to avoid
Meat and bones
Poultry and fish
Fatty food waste
Whole eggs
Dairy products
Human and pet feces
Pernicious weeds
Treated wood
http://www.illinoiswildflowers.info/
http://discountdogpoopbags.com/
https://ripenraworganics.com.au/

## Slide 11: Material preparation
Chop materials
  The smaller the pieces, the faster the process
Layer equal amounts of browns and greens
  Start and end with brown layers
Adjust moisture content
  Texture like a wrung-out sponge

## Slide 12: Compost pile maintenance
Maintain air and moisture
  Texture like a wrung-out sponge
Turn the pile at intervals
  More often for faster decomposition
  Less often for lower maintenance
Optionally, use instruments to
  Monitor temperature
  Monitor moisture
Maintain until compost is completely “finished”
  No recognizable materials
  Pile is completely cold
http://biogas.ifas.ufl.edu/SCC/basics.asp

## Slide 13: Infrastructure
Cost
Size (3’ x 3’ x 3’)
Ability to turn the pile
Pest resistance

## Slide 14: Site assessment
Convenient access
  Adding material
  Maintaining the pile
Not too wet
Not too sunny or dry
Protected from rodents
Near a water source
Near a “banked” supply of browns
http://www.frisss.hu/hirek/szombathelyen-is-elkezdodik-a-komposztalo-ladak-kiosztasa

## Slide 15: Critters in the compost pile
Most critters are beneficial

## Slide 16: Troubleshooting
Rodents | No action | A smelly pile
Meat Greasy or oily foods Cooked foods Physical access | Too dry C:N imbalance Pile not turned | Excess green (N) Too much water
http://amodernmother.com/2010/02/how-to-compost.html
https://www.allotment-garden.org/
www.learn.eartheasy.com

## Slide 17: Cold pile vs hot pile
Thermophilic 110-165F
Hot for a few days
Pros:
  Faster (weeks-months)
  Kill pathogens and weed seeds
Cons:
  More labor intensive
Mesophilic 70-110F
Medium temperatures
Pros:
  Less labor intensive
  More worm friendly
Cons:
  Slower (months-year)
Carbon to nitrogen ratio

## Slide 18: Using compost
Sift through ¼” sieve
Application
  1 to 2 inches for top dressing
  2 to 3 inches for incorporation
    Mix to a depth of 5 inches
  3+ inches for compost as mulch
http://www.charlesdowding.co.uk/no-dig-growing/
http://www.bhg.com/gardening/yard/garden-care/ten-steps-to-beginning-a-garden/

## Slide 19: Summary of some key points
Composting is getting on the right side of nature
The carbon to nitrogen ratio and moisture are the primary variables
The gardener can decide the amount of time and effort to put in
Composting and its results get better and easier with experience

## Slide 20: Vermicomposting Composting with worms
http://www.picshype.com/diy-wooden-worm-bin/worm-farm/28045
Don Krafft
Sara Johnson
UCCE Composting Education Program

## Slide 21: Why worm compost?
It’s good fun
Diverts waste products
Improves soil fertility
Reduces need for chemical fertilizer
Sequesters carbon
Suppresses pathogens
Very compact and can be done in limited spaces, including indoors
Produces a nutrient-rich soil amendment
Little or no expense
Very low maintenance

## Slide 22: Composting with worms
Most common composting worm: Red Wiggler (Eisenia fetida)
    Feeds from the duff layer
    Non borrowing
    Often referred to as Manure Worms
    Temperature range 55 – 77
Other worms: Red Worm (Lumbricus rubellus)
    Soil dwelling
    Requires more soil medium
    Prefers broken down material

## Slide 23: Creating an ideal worm habitat
Parameter | Range
Temperature | 40F to 95F The ideal range is 55F to 77F
Moisture | 40% to 60% Like a wrung-out sponge
Bedding | Safe and digestible
Food | Worm friendly
Light | None
https://www.armaghbanbridgecraigavon.gov.uk/dont-bin-itrecycle-your-food-waste/
https://unsplash.com/search/photos/darkness

## Slide 24: Setting up a worm bin
Acquire a bin
  Recycle bin
  Dresser drawer
  Commercial bin
Prepare the bin
  Provide air holes
  Provide drainage
Prepare the bedding
  Newspaper
  Cardboard
  Paper
http://compost.css.cornell.edu/worms/steps.html

## Slide 25: Setting up a worm bin (continued)
Moisten the bedding
  Use a spray bottle
Add some worms
  Get ‘em from a friend
  Buy them locally
  Buy them online
Bury food scraps under the bedding
  Select suitable worm food
Place a sheet of newspaper on top of the bedding
Cover the bin
http://compost.css.cornell.edu/worms/steps.html

## Slide 26: What to feed your worms
https://ar.pinterest.com/pin/566046246905685885/
Vegetables
Fruit and juicer pulp
Grains
Tea bags
Coffee & filters
Eggshells (ground)
Lawn clippings (if not sprayed)
Pasta
Newspaper
Cardboard
Sawdust (from untreated wood)

## Slide 27: What not to feed your worms
Meat, bones, and fat
Dairy products (except egg shells)
Canned processed food
Citrus
Onions and garlic
Spicy foods
Yard trimmings that have been treated
Glossy paper
Toxic plants
Anything that is not biodegradable
https://americanira.com/category/prohibited-transactions/

## Slide 28: Other types of bins
https://www.etsy.com/

## Slide 29: Harvesting vermicompost
Tray or bin
  Dump contents out onto a tarp
  Allow the worms to move down and away from the light
  Scrape a layer off the top
  Repeat and then recover worms
Long bin
  Feed on alternate sides of the bin
  Harvest from the other side
Flow-through system
  Release vermicompost from the bottom of the bin
https://crisonthesidelines.wordpress.com/2008/11/12/harvesting-vermicompost-2/

## Slide 30: Worm tunnels
https://deepgreenpermaculture.com/diy-instructions/build-a-worm-tunnel-vermicomposting-system/

## Slide 31: Troubleshooting
Lots of flies
Don’t overfeed
Keep food covered
Keep inside of bin covered with newspaper
Limit fruit
Cut food into small pieces for faster consumption
Smells bad
Provide more air
Control moisture
Mix the bedding with fresh, dry material
Drain leachate
My worms have died
Heat wave
Bin is too wet and worms are drowning
Bin is too dry and worms are drying out
Insufficient air
Turned into hot composter
No food
https://www.kaskus.co.id/thread/58381bfc1cbfaa1c418b456e/stres-bisa-bikin-sering-kentut-lho/
https://www.illustrationsource.com/
http://clipart-library.com/rip-cliparts.html

## Slide 32: Using vermicompost
Top-dress indoor, outdoor, vegetable, and landscaping plants
Spread it on a lawn
Add it to the soil between seasonal plantings
Add it to seed starting and up-potting mixes

## Slide 33: University of California Cooperative Extension (UCCE) Master Composters of Santa Clara County
Composting and vermicomposting workshops
  http://cesantaclara.ucanr.edu/Home_Composting_Education/Composting_Workshops/
Composting video series
  http://cesantaclara.ucanr.edu/Home_Composting_Education/Composting_Video_Series_/
Where to get compost
  http://cesantaclara.ucanr.edu/Home_Composting_Education/Where_to_Get_Compost/

## Slide 34: Thank You!
Don Krafft Sara Johnson UCCE Composting Education Program
www.ucanr.edu/compost
http://archive.constantcontact.com/fs197/1101811920551/archive/1117199404572.html
Insaneclopedia http://insaneclopedia.com/1415/antidepressant-microbes-soil-dirt-makes-happy/

## Slide 35: Outline
About compost
America’s garbage
Waste management hierarchy
Where do organics go?
Why compost?
What is compost?
Vermicomposting
Why worm compost?
Composting with worms
Creating habitat
Setting up a bin
What to feed worms
What not to feed worms
Types of bins
Harvesting
Worm tunnels
Trouble-shooting
Using vermicompost
How to make compost
Composting materials
Making compost
Where to compost
Critters in the compost
Trouble-shooting
Hot vs cold composting
Using compost